## Slide 1: ARMv8 Registers
Presenter :
Sudhanshu Gupta

## Slide 2
ARMv8 registers
AArch64 execution state provides 31 × 64-bit general-purpose registers accessible at all times and in all Exception levels.
Each register is 64 bits wide and they are generally referred to as registers X0-X30.
Each AArch64 64-bit general-purpose register (X0-X30) also has a 32-bit (W0-W30) form.

## Slide 3
ARMv8 General Purpose Registers (32bit / 64bit mode)
Each AArch64 64-bit general-purpose register (X0-X30) also has a 32-bit (W0-W30) form.
32-bit W register forms the lower half of the corresponding 64-bit X register.
That is, W0 maps onto the lower word of X0.
Reads from W registers disregard the higher 32 bits of the corresponding X register and leave
them unchanged.
Writes to W registers set the higher 32 bits of the X register to zero. That is,
writing 0xFFFFFFFF into W0 sets X0 to 0x00000000FFFFFFFF.

## Slide 4
AArch64 Special Registers
In addition to the 31 core registers, there are also several special registers.
Many instructions are encoded such that the number 31 represents the zero register, ZR (WZR/XZR).
Also a restricted group of instructions where one or more of the arguments are encoded such that number 31 represents the Stack Pointer (SP).
Note :
64-bit form of the SP register does not use an X prefix.

## Slide 5
AArch64 Special Registers
The Exception Return (ERET) state is held in the following dedicated registers for each Exception level:
• Exception Link Register (ELR).
• Saved Processor State Register (SPSR).
There is a dedicated SP per Exception level, but it is not used to hold return state

## Slide 6
AArch64 Special Registers - Zero Register
The zero register reads as zero when used as a source register [Read]
Discards the result when used as a destination register. [Write]
ZR can be used in most, but not all instructions.

## Slide 7
AArch64 Special Registers – Stack Pointer
Stack pointer variant to use is decided upon the current processor Execution Level.
By default, taking an exception selects the stack pointer for the target Exception level, SP_ELn
Each Exception level has its own stack pointer, SP_EL0, SP_EL1, SP_EL2, and SP_EL3.
For example, taking an exception to EL1 selects SP_EL1
t suffix indicates that the SP_EL0 stack pointer is selected
h suffix indicates that the SP_ELn stack pointer is selected.
When in AArch64 at an Exception level other than EL0, the processor can use either:
  A dedicated 64-bit stack pointer associated with that Exception level (SP_ELn).
  The stack pointer associated with EL0 (SP_EL0).

## Slide 8
AArch64 Special Registers – Program Counter
ARMv7 Drawback :
One feature of the original ARMv7 instruction set was the use of R15, the Program Counter (PC) as a general-purpose register.
PC enabled some clever programming tricks, but it introduced complications for compilers and the design of complex pipelines.
ARMv8 Enhancement :
Removing direct access to the PC in ARMv8 makes return prediction easier and simplifies the ABI specification.
PC is never accessible as a named register.
Its use is implicit in certain instructions such as PC-relative load and address generation.
PC cannot be specified as the destination of a data processing instruction or load instruction.

## Slide 9
AArch64 Special Registers – Exception Link Register (ELR)
The Exception Link Register holds the exception return address.

## Slide 10
AArch64 Special Registers - Saved Process Status Register (SPSR)
When taking an exception, the processor state is stored in the relevant Saved Program Status Register (SPSR),
SPSR holds the value of PSTATE before taking an exception and is used to restore the value of PSTATE when executing an exception return.
N Negative result (N flag).
Z Zero result (Z) flag.
C Carry out (C flag).
V Overflow (V flag).
SS Software Step.
IL Illegal Execution State bit.
D Process state Debug mask
A SError (System Error) mask bit.
I IRQ mask bit.
F FIQ mask bit.
M[4] Execution state that the exception was taken from. A value of 0 indicates AArch64.
M[3:0] Mode or Exception level that an exception was taken from.

## Slide 11
AArch64 Special Registers – Processor States
AArch64 does not have a direct equivalent of the ARMv7 Current Program Status Register (CPSR).
In AArch64, the components of the traditional CPSR are supplied as fields that can be made accessible independently.
These are referred to collectively as Processor State (PSTATE).
In AArch64, you return from an exception by executing the ERET instruction, and this causes the SPSR_ELn to be copied into PSTATE. This restores the ALU flags, execution state, Exception level, and the processor branches.
From here, you continue execution from the address in ELR_ELn.
PSTATE.{N, Z, C, V} fields can be accessed at EL0.
All other PSTATE fields can be accessed at EL1 or higher and are UNDEFINED at EL0.

## Slide 12
AArch64 Special Registers – System Registers
System Configuration is controlled through system registers
Accessed using MSR and MRS instructions
The name of a register tells you the lowest Exception level that it can be accessed from.
For example:
• TTBR0_EL1 is accessible from EL1, EL2, and EL3.
• TTBR0_EL2 is accessible from EL2 and EL3.
Registers that have the suffix _ELn have a separate, banked copy in some or all of the levels, though usually not EL0.
Moslty System Registers are not accessible from EL0. Few system registers are accessible from EL0, although the Cache Type Register (CTR_EL0) is an example of one that can be accessible.
Code to access system registers takes the following form:
MRS x0, TTBR0_EL1 // Move TTBR0_EL1 into x0
MSR TTBR0_EL1, x0 // Move x0 into TTBR0_EL1

## Slide 13
AArch64 Special Registers – System Registers – System Control Register
System Control Register controls
Standard memory,
System facilities and
Provides status information for functions that are implemented in the core.
Not all bits are available above EL1

## Slide 14
AArch64 Special Registers – System Registers – System Control Register
Bit | Description
UCI | When set, enables EL0 access in AArch64 for DC CVAU, DC CIVAC, DC CVAC, and IC IVAU instructions.
EE | Exception endianness. 0 Little endian. 1 Big endian.
EOE | Endianness of explicit data accesses at EL0. 0 Explicit data accesses at EL0 are little-endian. 1 Explicit data accesses at EL0 are big-endian.
WXN | Write permission implies XN (eXecute Never). 0 Regions with write permission are not forced to XN. 1 Regions with write permission are forced to XN.
nTWE | Not trap WFE. A value of 1 means that WFE instructions are executed as normal.
nTWI | Not trap WFI. A value of 1 means that WFI instructions are executed as normal.
UCT | When set, enables EL0 access in AArch64 to the CTR_EL0 register
DZE | Access to DC ZVA instruction at EL0 0 Execution prohibited. 1 Execution allowed.
I | Instruction cache enable.
UMA | User Mask Access. Controls access to interrupt masks from EL0, when EL0 is using AArch64.
SED | SETEND Disable. Disables SETEND (Set Endianness) instructions at EL0 using AArch32. 0 SETEND instructions are enabled. 1 The SETEND instruction is disabled.

## Slide 15
AArch64 Special Registers – System Registers – System Control Register
Bit | Description
ITD | IT (If Then Instruction) Disable. The possible values of this bit are: 0 The IT instruction is available. 1 The IT instruction is treated as a 16-bit instruction. Only another 16-bit instruction, or the first half of a 32-bit instruction, can follow.
CP15BEN | CP15 barrier enable. If implemented, it is an enable bit for the AArch32 CP15 DMB, DSB, and ISB barrier operations.
SA0 | Stack Alignment Check Enable for EL0.
SA | Stack Alignment Check Enable.
C | Data cache enable. This is an enable bit for data caches at EL0 and EL1. Data accesses to cacheable Normal memory are cached.
A | Alignment check enable bit.
M | Enable the MMU

## Slide 16
AArch64 Special Registers – Processor State

## Slide 17
AArch64 Special Registers – Endianness / Byte Ordering
two basic ways of viewing bytes in memory
Little-Endian (LE) or
Big-Endian (BE).
On big-endian machines, the most significant byte of an object in memory is stored at the lowest address
On little-endian machines, the least significant byte is stored at the lowest address
Endianness is controlled independently for each EL3,2,1 via
SCTLR_ELn.EE = 0  LittleEndian
SCTLR_ELn.EE = 1  BigEndian
At EL1, SCTLR_EL1.E0E controls the data endianness setting for EL0.

## Slide 18
AArch64 Special Registers – NEON and floating-point registers